## Slide 1: Renewable Ammonia: Kenya’s Business Case
Report Launch Event
April 2025
REPORT SERIES
CLEAN HYDROGEN PROJECTS IN THE GLOBAL SOUTH
Notes: Thank you Susana, and welcome on my part as well to the presentation of our report, 'Renewable Ammonia: Kenya’s Business Case.'

## Slide 2: Hydrogen opportunity
Notes: The production of renewable, hydrogen-based ammonia presents a major opportunity for Kenya's socio-economic development. In this report, we explore viable business cases linked to specific locations across the country.

## Slide 3: Kenya's hydrogen opportunity
Opportunities
Kenya’s hydrogen strategy
2023 – 2027
2028 – 2032
2032 and beyond
Local value creation and economic development.
Increased independence from global fertilizer markets.
Industrial decarbonization across key sectors, including fertilizer production, mining operations, and steel manufacturing.
Enhanced energy infrastructure and improved access to energy.
Kenya as a front runner in the African hydrogen economy
Domestic market development
Renewable fertilizer production target: 100,000 tons per year
Domestic market growth
Renewable fertilizer production target: >300,000 tons per year
Domestic and export market growth
Notes: Key development opportunities associated with hydrogen projects include…
In a parallel piece of research, we conducted a clustering analysis of African countries to analyze their socio-economic potential to develop a hydrogen sector. Kenya emerged as a front runner in this analysis, being … (report will be launched in a couple of weeks)
Kenya launched a hydrogen strategy in 2023 to support this development: Strategic emphasis on domestic renewable fertilizer production with production targets of 100 ktons by 2027 and over 300 ktons by 2032.

## Slide 4: Building viable business cases for renewable hydrogen in Kenya
Current hydrogen projects in Kenya
Advancing Kenya's hydrogen economy
Current projects focus on renewable fertilizer production.
4/5 projects are still in the feasibility stage.
Talus Renewables is the only operational project, producing renewable fertilizer at a small scale.
Planned projects are centered around Lake Naivasha and Mombasa.
What do viable business cases for renewable hydrogen in Kenya look like?
Where should new renewable hydrogen projects be located?
What are success factors for new hydrogen projects?
Notes: Currently planned hydrogen projects are in line with this strategy, focusing on renewable ammonia production.
Project location
However: 4/5 projects are still in feasibility stage.
In this report we ask: Where are suitable locations for renewable-hydrogen based ammonia production in Kenya and under which circumstances can these projects make viable business models?

## Slide 5: Our research
Notes: Let me present our research methodology to you.

## Slide 6: Methodology
Spatial resolution: 50x50m
Solar and wind
Electrolysis
Ammonia production
Battery and hydrogen
storage
Grid expansion
GIS analysis to identify suitable locations
Kenyan stakeholder workshop to identify favorable locations
Site optimization and financial analysis
to simulate viable business cases
Identify conditions for economically viable hydrogen projects
GIS analysis: https://maps.iee.fraunhofer.de/ptx-kenya-atlas/
Notes: What does it take to produce renewable ammonia? Bottom-left: visualization
First step: GIS-based assessment of the renewable energy potential in Kenya, to identify suitable locations for project development.
Subsequently, online workshop with local stakeholders.
Then, optimized technical configuration & conducted financial analysis.
I’ll now hand over to Benedikt from the Fraunhofer IEE, who will delve into the findings from the GIS-based renewable energy potential analysis, using an interactive visualization of the results.

## Slide 7: RE potential open-source webtool

## Slide 8: Analysis
Notes: Thank you Benedikt, for these insights into the renewable energy potential analysis. Let’s start into the analysis of the identified locations.

## Slide 9: Four Kenyan regions highly suitable for anchoring renewable ammonia projects
Characteristics of selected regions
Suitable
Limited
Turkana Central
Turkana South
Kisumu
Mombasa
Characteristics of excluded regions
Sufficient renewable energy potential to operate a 500 MW electrolyzer
Sufficient water availability from open-water sources
Non-conflicting land use
Transport and electric infrastructure in proximity
Offtake opportunities for renewable hydrogen-based products
Insufficient renewable energy potential or water availability
Land-use conflicts
Remote location with no infrastructure or offtake opportunities for renewable hydrogen-based products
Notes: As Benedikt presented, we have selected four suitable locations for renewable hydrogen-based ammonia production.
All these locations combine: a) sufficient renewable energy potential to operate a 500 MW electrolyzer, b) sufficient water availability, c) non-nonflicting land-use, d) transport and electric infrastructure in proximity, which can be utilized and extended, as well as e) offtake opportunities for renewable hydrogen-based products.
We begin our analysis at Lake Turkana.

## Slide 10: Turkana Central
Major road
Suitable
Limited
25 km
Lake Turkana Wind Power (LTWP) 310 MW
Nairobi
450km
Uganda
85km
Ethiopia
100km
Located in northern Kenya, to the western side of Lake Turkana.
Extensive potential for solar and hybrid (wind and solar) energy around the city of Lodwar.
The region itself does not have significant offtake potential for renewable hydrogen-based goods such as ammonia or fertilizer.
Proximity to the city of Lodwar provides access to transport infrastructure and everyday goods for workers.
Electric grid infrastructure is accessible to the south of Lake Turkana in 170km distance, offering sufficient capacity to supply electrolyzers of up to 100 MW.
Sufficient water for hydrogen production is available through Lake Turkana or the Turkwell River.
Notes: Location & renewable energy potential.
Offtake: not significant, further offtake opportunities in the South.
Electric infrastructure: transmission line South of Lake Turkana, capable of supplying a 100MW electrolyzer
City of Lodwar: Transport infrastructure and everyday goods for workers.

## Slide 11: Turkana Central
EUR 66 Mio.
EUR 489 Mio.
EUR 2,107 Mio.
6,500 t-NH3/year
62,800 t-NH3/year
303,000 t-NH3/year
Total investment costs
Annual ammonia production
Notes: Different project sizes: 10MW, 100MW, and 500MW.
Total investment costs range: EUR 66 Mio. to EUR 2.1 Billion
Annual production ranges: 6,500 t-NH3 / year (10 MW) to ca. 300,000 t-NH3 / year (500 MW).
LCOA ranges: 1,876 EUR/t (10 MW) to 1,289 EUR/t (500 MW)  Scaling to 500MW leads to a cost decrease of ca. 30%
RE costs make up: 40% (10MW) to 60% (500MW)

## Slide 12: Turkana South
Lake Turkana Wind Power (LTWP) 310 MW
Nairobi
350km
Major road
High-voltage line
Suitable
Limited
50 km
Located in northern Kenya, to the south of Lake Turkana and within the geothermally active Rift Valley.
Extensive potential for solar, wind and hybrid (wind and solar) energy. Presumably also geothermal energy potential, which would have to be confirmed by on-site test drills.
The region itself does not have significant offtake potential for renewable hydrogen-based goods such as ammonia or fertilizer.
Major roads run through the identified region, providing the required transport infrastructure.
Connection to the national electricity grid could be enabled via a transmission line running through the region, offering sufficient capacity to supply electrolyzers of up to 100 MW.
Sufficient water for hydrogen production is available through Lake Turkana.
Notes: Location and renewable energy potential.
Offtake: not significant, further offtake opportunities in the South.
Electric infrastructure: transmission line South of Lake Turkana, capable of supplying a 100MW electrolyzer (same as for Lake Central)
Infrastructure: Major roads run through the potential region, providing the required transport infrastructure.

## Slide 13: Turkana South
EUR 54 Mio.
EUR 381 Mio.
EUR 1,630 Mio.
7,100 t-NH3/year
65,500 t-NH3/year
310,500 t-NH3/year
Total investment costs
Annual ammonia production
Notes: Total investment costs range: EUR 54 Mio. to EUR 1.6 Billion (lower than Turkana Central)
Annual production ranges: 7,100 t-NH3 / year (10 MW) to ca. 311,000 t-NH3 / year  Higher than Turkana Central
LCOA is lower than in Turkana Central! 1,468 EUR/t (10 MW) to 999 EUR/t (500 MW)  Lowest LCOA across all regions due to best RE potential!

## Slide 14: Kisumu
Located in western Kenya, at the shoreline of Lake Victoria.
Extensive potential for solar energy only.
Proximity to Kenya’s 3rd largest city provides access to transport infrastructure and everyday goods for workers.
The region bears significant potential for the offtake of renewable hydrogen-based ammonia and fertilizer to local industries and agriculture. Furthermore, export opportunities exist through Lake Victoria to neighboring countries.
Sufficient water for hydrogen production is available through Lake Victoria.
Although an electric grid infrastructure exists in the region, its capacity and reliability is too low to facilitate reliable transmission of renewable electricity to electrolyzers.
Suitable
Limited
Major road
High-voltage line
25 km
Alten (44 MW), Radiant (40 MW), Eldosol (40 MW) Solar Power Plants
90km
Nairobi
260km
Kopere Solar Power Plant (50 MW)
50 km
KISIMU
HOMA BAY
Notes: Location and renewable energy potential.
Offtake: Good potential, either through Lake Viktoria or to close-by industries around Kisumu or Nairobi, which is located ca. 260 km to the East.
Infrastructure: Insufficient electric infrastructure to serve the needs of ammonia production projects. However, good transport infrastructure exists.
Water availability

## Slide 15: Kisumu
EUR 47 Mio.
EUR 340 Mio.
EUR 1,357 Mio.
3,400 t-NH3/year
32,400 t-NH3/year
157,900 t-NH3/year
Total investment costs
Annual ammonia production
Notes: Total investment costs range: EUR 47 Mio. to EUR 1.4 Billion
Annual production ranges: 3,400 t-NH3 / year (10 MW) to ca. 160,000 t-NH3 / year (lowest across all regions)
2,437 EUR/t (10 MW) to 1,505 EUR/t (500 MW)  LCOA is highest across all regions!

## Slide 16: Mombasa
Located in southeastern Kenya, along the country’s Indian Ocean coast.
Extensive potential for wind energy and – in a few locations – for hybrid renewable energy (wind and solar).
The region bears significant potential for the offtake of renewable hydrogen-based ammonia and fertilizer to local industries and agriculture. Furthermore, export opportunities to international markets exist through the port of Mombasa.
Proximity to Kenya’s 2nd largest city provides access to transport infrastructure and everyday goods for workers.
The existing electric grid offers sufficient capacity to supply electrolyzers of up to 500 MW.
Sufficient water for hydrogen production is available through desalination of Indian Ocean sea water.
Malindi Solar Power Plant (52 MW)
Nairobi
440km
Kilifi Wind Farm (36 MW)
MOMBASA
Suitable
Limited
Major road
High-voltage line
25 km
Notes: Location and renewable energy potential.
Offtake: Good offtake opportunities, through the port of Mombasa or to close-by domestic industries.
Electric infrastructure: Capable of supplying electricity to large-scale electrolysis plants. Significant advantage!
Proximity to the urban area of Mombasa (infra & workers).
Water is available through potential desalination of water from the Indian ocean.

## Slide 17: Mombasa
EUR 58 Mio.
EUR 430 Mio.
EUR 1,813 Mio.
6,400 t-NH3/year
60,200 t-NH3/year
291,300 t-NH3/year
Total investment costs
Annual ammonia production
Notes: Total investment costs range: EUR 58 Mio. to EUR 1.8 Billion
Annual production ranges: 6,400 t-NH3 / year (10 MW) to ca. 290,000 t-NH3 / year
LCOA ranges: 1,720 EUR/t (10 MW) to 1,201 EUR/t (500 MW)  2nd lowest across all regions
Together with extensive existing electric and transport infrastructure: One of the most suitable regions!
HOWEVER: None of the simulated locations is cost-competitive with current market prices for conventional ammonia! (~400-500 €/t-NH3)
THEREFORE: We are looking at the production of ammonia-based fertilizer as a value-added product to capture this remaining green premium.

## Slide 18: Domestic fertilizer market offtake opportunities
Renewable hydrogen-based fertilizers have the potential to be cost-competitive in Kenya’s domestic market, offering a more stable and secure supply at reduced and less volatile prices.
Domestic retail fertilizer prices in Kenya significantly exceed global market levels.
During the global energy crisis in 2022, domestic fertilizer prices rose by 20 – 60% compared to preceding and subsequent years.
The estimated production cost of renewable fertilizers – based on locally produced hydrogen – is lower than the domestic retail prices recorded in 2022 across all fertilizer types.
Renewable hydrogen-based fertilizers also demonstrate potential to undercut recent retail prices (as of 2024) for DAP, NPK, and CAN.
Chart: Cost in EUR/t
| DAP | NPK | Urea | CAN
Global market price | 553.6077 | 353.8168 | 286.0306 | 234.3606
Retail price in Kenya | 784.2775 | 738.1436 | 645.8756 | 511.9026
Retail price in Kenya | 955.3423 | 887.6176 | 1039.3061 | 830.7806
Renewable fertilizer cost | 539.7903 | 662.6912 | 741.6481 | 435.6187
Renewable fertilizer cost | 647.6603 | 770.5612 | 1008.9781 | 595.0787
2022
2024
2022
2022
2022
2024
2024
2024
Max
Max
Max
Max
Min
Min
Min
Min
DAP
NPK
Urea
CAN
Notes: Domestic retail fertilizer prices in Kenya significantly exceed global market levels.
Furthermore, prices are volatile and dependent on global market dynamics. Rise during the energy crisis in 2022 by 20-60%!
Domestic renewable, ammonia-based fertilizer production could stabilize these price fluctuations AND undercut average fertilizer prices.
In turn, this leads to increased price stability at a lower cost for regional consumers, while simultaneously offering a viable business case for renewable ammonia projects in Kenya!

## Slide 19: Recommendations

## Slide 20: Recommendations
Turkana Central
Turkana South
Kisumu
Mombasa
1,289-1,876
999-1,468
1,505-2,437
1,201-1,720
LCOA [EUR/ton-NH2]
Mombasa and Turkana South and most favorable, combining potential for low-cost hydrogen production with infrastructure availability and offtake opportunities.
Locations
Fertilizer opportunity
Financial support instruments
Enablers
Renewable hydrogen-based fertilizers have the potential to be cost-competitive in Kenya’s domestic market.
Renewable ammonia projects need to address green premium and long-term offtake certainty, while renewable fertilizer projects seek to mitigate market price risks.
High cost of capital and lack of infrastructure constitute key project development barriers.
Notes: Most-suitable locations: Mombasa and Turkana South
I want to emphasize the opportunity that lies in the domestic fertilizer market: a) It can absorb green premium of ammonia production; b) renewable fertilizer would undercut current market prices, offer increased price stability.
Financial support: a) green premium + long-term offtake for ammonia; b) market price risks for fertilizer
Enablers: a) decrease of the cost-of-capital; b) improvement of infrastructure

## Slide 21
April 2025
Julian Reul
Program Lead Research
T: +49 40 36197500
E: julian.reul@h2-global.org
www.h2-global.org
H2Global library
Copyright ©2025 H2Global Stiftung. All rights reserved.
Disclaimer: This publication is for informational purposes only and does not constitute any warranty, guarantee, or liability for H2Global Stiftung, its subsidiaries, or affiliates.